## Slide 1: Applicability of Abstraction and Control of Traffic Engineered Networks (ACTN) to Packet Optical Integration (POI) service assurance draft-poidt-teas-actn-poi-assurance-00
Authors
Italo Busi – Italo.busi@huawei.com
Daniel King – daniel@olddog.co.uk
Jean-Francois Bouquier – jeff.bouquier@vodafone.com
Fabio Peruzzini – fabio.peruzzini@telecomitalia.it
Paolo Volpato – paolo.volpato@huawei.com
Prasenjit Manna – prmanna@cisco.com

## Slide 2: ACTN POI Next Steps - Overview
ACTN POI (step 1)
Inventory, Service and Topology Discovery
Establishment of L2VPN/L3VPN with TE requirements
ACTN POI (step 2a) – service assurance
Optical Network failures and degradation
IP/Optical Edge failures
ACTN POI (step 2b) – pluggable
Pluggable WDM interfaces on routers
Same scenarios as in step 1
TEAS WG
CCAMP WG

## Slide 3: ACTN POI Next Steps - Motivation
Interest from operators to analyse applicability of ACTN to additional POI capabilities/architectures
  Service assurance
  Pluggable WDM interfaces on the routers
Why new drafts?
  Not to overweight the current draft
  Difference level of maturity of the content
Why different WGs?
  POI service assurance impacts both IP and Optical technologies  TEAS WG scope
  Pluggable impacts O-PNC and P-PNC for optical tunnel setup  CCAMP WG scope
Keep CCAMP, TEAS and OPSAWG updated

## Slide 4: ACTN POI Service Assurance - Use Cases
  1. Optical Network failures and degradation
      Fault Detection
      Performance Monitoring
      Protection Switching
      Maintenance
  2. IP/Optical Edge failures (router port or router node failures)
      Fault detection
      Protection switching
Packet Domain 1
Packet-PNC 1
Optical-PNC 1
Optical-PNC 2
Packet-PNC 2
MDSC
Packet Domain 2
Optical Domain 1
Optical Domain 2
CE
CE
PE
BR
BR
PE
Figure 1 - Reference Scenario

## Slide 5: Status and Next Steps
Draft -00 is just an outline
  Show planned next steps on ACTN POI
  Get interest to join this work
Issue tracking and current version available on Git
  https://github.com/italobusi/draft-poidt-teas-actn-poi-assurance
Discuss all ACTN POI drafts during the weekly ACTN POI calls
Next Steps:
  Work on a more substantial content for the draft

## Slide 6: Backup

## Slide 7
IP and DWDM protection coordination - network resiliency
SDN controller must be able to reroute traffic at IP and DWDM layer, after an unexpected physical fault
Coordination between IP and DWDM protections should be able to guarantee a better service availability
SDN controller must be aware of the change in topology and must take consequent action to protect the traffic at both IP and DWDM layer
P1
R1
ROADM 1
ROADM 2
ROADM 3
R2
R3
P1
P2
P2
P1
P2
X
Problem Statement, value added by SDN:
Expected benefits:
Better and easier control of network resources, easier and more efficient planning of network protections  OPEX and CAPEX reduction
IP services less impacted by faults DWDM network better service availability at the same CAPEX
INITIAL CONDITION
SDN controller knows network topology at both IP and optical layer, and is also aware of interconnection links. The IP link R1/p1-R2/p1 (BLUE) , R1/p2-R3/p1 (YELLOW) and R3/p2-R2/p2 (GREEN) are already provisioned
TEST DETAIL
Fiber cut on DWDM section transporting BLUE IP link IP traffic (FRR protection) must be restored in below that 50ms DWDM link must be restored in few minutes After DWDM link is restored, SDN controller moves back the traffic on the BLUE dashed IP link without traffic impact When the faulty DWDM link is restored, , before the revert of the OCH takes place, SDN controller has to move IP traffic to the YELLOW and GREEN links. After the WSON has reverted the OCH link to the original path (BLUE), SDN controller moves IP traffic to the BLUE link (all operations must be hitless on traffic)

## Slide 8
IP and DWDM protection coordination - network resiliency during maintenance events
Before planned maintenance operation on DWDM network takes place, IP traffic should be moved hitless to another link
SDN controller must reroute IP traffic before the events takes place. It should be possible to lock IP traffic to the protection route until the maintenance event is finished, unless a fault occurs on such path
P1
P2
Problem Statement, value added by SDN:
INITIAL CONDITION
SDN controller knows that the DWDM link, carrying IP link R1/p1-R2/p1 (BLUE) will go in maintenance operation at a specified time
TEST DETAIL
Few minutes before the maintenance window, SDN controller reroutes hitless all IP traffic passing on BLUE IP link to the YELLOW and GREEN IP links Fiber cut (maintenance) on the DWDM section has no impact on traffic WSON restore the OCH link and doesn’t revert to the original link until the maintenance window is finished 4a. IP traffic is locked to the protection path, unless a fault occurs, until maintenance window is finished, then SDN controller moves back the IP traffic hitless after WSON has reverted to the original path 4b. When the WSON restore the OCH link, IP traffic has to be moved back to the new IP LINK (BLUE dashed). When the maintenance window is concluded, before the revert of the OCH takes place, SDN controller has to move IP traffic to the YELLOW and GREEN links. After the WSON has reverted the OCH link to the original path (BLUE), SDN controller moves IP traffic to the BLUE link (all operations must be hitless on traffic)
R1
ROADM 1
ROADM 2
ROADM 3
R2
R3
P1
P2
P1
P2
Expected benefits:
IP services not affected by maintenance operation on DWDM network better service availability at the same CAPEX

## Slide 9
Router port failure – 1:N “protection
Ability to distinguish failures (IP port failure or transport network failure)
In case of IP port failure, reuse of same ROADM optical resources (lambda, optical path) and reuse of remote IP port
Reduce IP interfaces over-provisioning and save optical channels interfaces and spectrum occupation  CAPEX reduction
Problem Statement, value added by SDN:
INITIAL CONDITION
SDN controller knows network topology at both IP and optical layer, and is also aware of interconnection links. The IP link R1/p1-R2/p1 (GREEN) is already provisioned.
TEST DETAIL
Fault on R1/p1, or on the interconnection link with the ROADM1 R1 copies failed port configuration (IP address, routing policy etc) on the stand-by port SDN controller tears down green optical channel SDN controller activates a new optical channel between R1/p2 IP port and the original one on R2, using original lambda and optical path SDN controller creates new IP link (GREEN dashed) between R1/p2 and R2/p1
R1
ROADM 1
ROADM 2
ROADM 3
R2
R3
Stand-by port
P1
P1
P2
Expected benefits:

## Slide 10
Dual-homing and node failure
Ability to distinguish failures (IP node failure or transport network failure)
In case of IP core node failure, re-route optical resources and reuse local edge IP port
Reduce IP edge interfaces over-provisioning and save optical channels interfaces and spectrum occupation  CAPEX reduction
R1
ROADM 1
ROADM 2
ROADM 3
R2
R3
Edge node
Backup port
Backup Core node
Main Core node
P1
P1
P1
INITIAL CONDITION
SDN controller knows network topology at both IP and optical layer, and is also aware of interconnection links. The IP link R1/p1-R2/p1 (GREEN) is already provisioned. R2 is main core node, R3 is backup node
TEST DETAIL
Fault on R2, or on the interconnection link with the ROADM2 SDN controller knows that there is a backup node, and creates the connectivity from R1/p1-R3/p1 using the same interface in R1 and ROADM1. SDN controller tears down GREEN optical channel SDN controller activates a new optical channel between R1/p1 IP port and R3/p1 SDN controller creates new IP link (GREEN dashed) between R1/p1 and R3/p1
Problem Statement, value added by SDN:
Expected benefits:

## Slide 11
Alert in case of degrade of DWDM link performance
SDN controller must be able to monitor DWDM links optical performances, and alert the operator in case of BER PRE-FEC values over a specified threshold
The warning about BER PRE-FEC threshold crossing should be related di IP links
Problem Statement, value added by SDN:
Expected benefits:
Automatic optical degrade avoidance  better service availability at the same CAPEX
INITIAL CONDITION
SDN controller knows network topology at both IP and optical layer, and is also aware of interconnection links. The IP links R1/p2-R2/p2 (BLUE) and links R1/p1-R2/p1 (GREEN) are already provisioned. Both DWDM links have acceptable BER pre-FEC values. Operator can chose a specified threshold of BER pre-FEC, that will trigger an alert on SDN controller
TEST DETAIL
Operator can choose the desired threshold of BER pre-FEC for the trigger of the alert condition When the threshold is crossed, an alert related to the involved IP links must be shown on SDN controller
P1
P2
R1
ROADM 1
ROADM 2
ROADM 3
R3
R2
P1
P2
BER pre-FEC > x
BER pre-FEC < x